## Slide 1
Interactive Computational Platform & Multi-Material Comparative Analysis of Cp(T) Behavior
GUI Engineering, Real-Time Plotting Engine & Engineering Application Case Studies
Prepared by: Student 2 (Group Member B)
Specialization: Interactive Web Systems, Canvas Graphic Algorithms, Materials Selection & Video Walkthrough
Course: Materials Thermodynamics and Computation

## Slide 2
[SYS-01] Computational Platform Architecture & Technology Stack
Client-side high-performance computing, standalone zero-dependency web execution
Software System Architecture:
• Zero-Dependency Standalone Runtime: Self-contained HTML5/JavaScript application (index.html) requiring no external CDN scripts, node modules, or server processes.
• Embedded Memory Database: The complete 230-material JSON dataset is loaded directly in browser memory, enabling sub-millisecond query execution.
• Built-in HTML5 Canvas Renderer: Native 2D canvas plotting engine with double-buffered rendering, dynamic grid scaling, and zero network latency.
• Companion Streamlit Python Dashboard: Companion data science platform (app.py) featuring Plotly integration for Python computational workflows.
Execution Pipeline & Event Loop:
✔ 1. Event Dispatcher: Listens to user inputs (search, category select, temp range, unit toggles, reference T slider).
✔ 2. State Manager: Maintains active selected material IDs, current temperature unit (K/C), and target specific heat unit.
✔ 3. Calculation Dispatcher: Polymorphic solver dynamically executes Shomate or polynomial algorithms across 100 discrete sampling points.
✔ 4. Viewport Renderer: Re-renders canvas gridlines, curve paths, warning alerts, ranking table, and citation cards at 60 FPS.

## Slide 3
[GUI-02] Canvas Plotting Algorithms & Coordinate Mapping Math
Mathematical transformation of physical thermodynamic coordinates to viewport canvas space
Coordinate Transform Mathematics:
• X-Axis Mapping Formula: X_canvas = Pad_left + ((T_disp - X_min) / (X_max - X_min)) * Width_plot Linearly maps temperature to pixel domain.
• Y-Axis Inversion Mapping Formula: Y_canvas = Pad_top + Height_plot - ((Cp - Y_min) / (Y_max - Y_min)) * Height_plot Accounts for inverted computer graphics Y-axis.
• High-DPI Display Scaling: Canvas scales by window.devicePixelRatio (2x on Retina/4K displays) to prevent line blurriness.
Interactive Raycasting & Hover Data Tips:
✔ Mouse Event Raycasting: Tracks mousemove coordinates (e.clientX, e.clientY) and reverses mapping to calculate exact hover temperature T_hover.
✔ Real-Time Evaluation: Dynamically evaluates Cp(T_hover) across all active curves simultaneously.
✔ HTML Tooltip Injection: Renders floating tooltip box tracking cursor position with formatted material names, formulas, and numeric coordinates.
✔ Viewport Auto-Resizing: Window resize listener recalculates canvas dimensions dynamically on display geometry changes.

## Slide 4
[SYS-03] Interactive Workflows & Multi-Unit Conversion Engine
Dimensional analysis routines, category filtering, and preset management
Interactive Control Workflows:
• Fuzzy Search Filtering: Instant sub-millisecond substring matching querying material name, formula, or category simultaneously.
• Active Tag Management: Visual color-coded tag tray allowing users to inspect active materials, toggle visibility, or delete traces individually.
• Quick Preset Buttons: • 'Metals': Loads 6 benchmark metals • 'Ceramics': Loads 6 structural ceramics • 'Multi-Class': Loads 8 representative materials across all classes • 'Clear': Flushes plotting tray in 1 click.
Multi-Unit Conversion Engine:
✔ Specific vs. Molar Duality: Automated molecular weight normalization: Cp_specific [J/(kg*K)] = (Cp_molar [J/(mol*K)] / M_w) * 1000
✔ Dual Temperature Scaling: Converts Kelvin <-> Celsius with automated input field rescaling: T [C] = T [K] - 273.15
✔ 5 Supported Units: • J/(kg*K) [SI Specific] • J/(mol*K) [SI Molar] • kJ/(kg*K) • cal/(g*C) [Metric Thermal] • BTU/(lb*F) [Imperial Aerospace]

## Slide 5
[SYS-04] Dynamic Property Ranking & Safety Warning Engine
Real-time sorting leaderboard and automated extrapolation boundary detection
Dynamic Reference T Ranking Engine:
• Interactive Reference Slider: Real-time slider (100 K to 2500 K) allowing continuous variation of reference temperature Tref.
• Array Sorting Algorithm: Dynamically evaluates Cp(Tref) across active materials and executes descending sort: items.sort((a, b) => b.cp - a.cp)
• Instant Leaderboard Rendering: Updates HTML table with Rank (#1, #2...), Material Name, Chemical Formula, and exact numeric Cp value in chosen unit.
Automated Extrapolation Warning Engine:
✔ Range Assertion Algorithm: Checks current viewport temperature boundaries [tMin, tMax] against calibrated limits [m.T_min, m.T_max].
✔ Visual Alert Trigger: If any plotted material extends outside verified bounds, an amber alert banner is dynamically rendered to alert the user.
✔ Engineering Defense: Prevents students and engineers from making decisions based on unconstrained polynomial extrapolation artifacts.

## Slide 6
[CASE-01] Engineering Case Study 1: Aerospace Airframe Materials
Thermal inertia, heating rates, and material selection tradeoffs
Materials Compared:
• Aluminum Alloy 7075-T6: Cp(298 K) = 960 J/(kg*K) [Valid: 273 - 750 K]
• Titanium Ti-6Al-4V (Grade 5): Cp(298 K) = 526 J/(kg*K) [Valid: 298 - 1250 K]
• Inconel 718 Superalloy: Cp(298 K) = 435 J/(kg*K) [Valid: 298 - 1300 K]
• CFRP Carbon/Epoxy (60% vf): Cp(298 K) = 1100 J/(kg*K) [Valid: 200 - 450 K]
Engineering Selection Findings:
✔ Thermal Inertia & Temperature Rise Rate: dT/dt = q_in / (rho * Cp * Volume) Titanium and Inconel heat up >2x faster than Aluminum for identical thermal flux due to low Cp.
✔ Aerospace Skin Damping: High specific heat of CFRP provides advantageous thermal damping during short-duration aerodynamic heating surges.
✔ High-Temperature Retention: Inconel 718 maintains structural stability up to 1300 K, while Al 7075 loses strength above 450 K.

## Slide 7
[CASE-02] Engineering Case Study 2: Gas Turbine Thermal Barrier Coatings
Multi-layer thermal insulation stack optimization in modern jet engines
TBC Architecture Layers:
• Topcoat: 8YSZ (8 wt% Yttria-Stabilized Zirconia) Cp ~ 520 J/(kg*K), k ~ 2.0 W/(m*K), stable to 2200 K.
• Thermally Grown Oxide (TGO): Corundum Al2O3 Cp ~ 790 J/(kg*K), forms dense diffusion barrier.
• Superalloy Substrate: Inconel 718 / 625 Core Cp ~ 410 J/(kg*K), high creep resistance.
Thermal Diffusivity Analysis:
✔ Thermal Diffusivity Synergy: alpha = k / (rho * Cp) Low thermal conductivity combined with moderate volumetric heat capacity (rho*Cp) of YSZ suppresses transient heat penetration into turbine blades.
✔ Thermal Expansion Match: Smooth monotonic Cp curve of Al2O3 TGO minimizes interfacial thermal fatigue stress during engine throttle acceleration cycles.
✔ Phase Stability: 8YSZ prevents detrimental monoclinic phase transformation up to 1478 K.

## Slide 8
[CASE-03] Engineering Case Study 3: Hypersonic UHTC Leading Edges
Extreme enthalpy absorption and stagnation thermal protection
UHTC Materials Evaluated:
• Hafnium Carbide (HfC): Tm = 4173 K, Cp(298 K) = 37.4 J/(mol*K)
• Tantalum Carbide (TaC): Tm = 4153 K, Cp(298 K) = 36.8 J/(mol*K)
• Zirconium Diboride (ZrB2): Tm = 3523 K, Cp(298 K) = 48.2 J/(mol*K)
• Ta4HfC5 Intermetallic: Tm ~ 4263 K, Cp(298 K) = 192 J/(mol*K)
Hypersonic Selection Findings:
✔ Ablative Heat Sink Superiority: ZrB2 and HfB2 possess 3-atom unit cells yielding higher asymptotic molar heat capacity (3 * 3R = 9R) than mono-carbides (2 * 3R = 6R).
✔ Enthalpy Absorption: Total enthalpy absorbed H(3000 K) - H(298 K) is over 2.5x greater in diborides, providing maximum thermal buffering in shock stagnation zones.
✔ Oxidation Resistance: Forms self-healing B2O3 glass scale under aerodynamic shear.

## Slide 9
[CASE-04] Engineering Case Study 4: EV Battery Thermal Management
Heat capacity buffering against thermal runaway in lithium-ion cathodes
Cathode Chemistries Investigated:
• LiCoO2 (LCO): Mobile consumer cathode, Cp(298 K) = 770 J/(kg*K)
• LiFePO4 (LFP): High-safety olivine EV cathode, Cp(298 K) = 751 J/(kg*K)
• NMC-811: High-energy EV cathode, Cp(298 K) = 980 J/(kg*K)
• Li4Ti5O12 (LTO Anode): Fast-charging anode, Cp(298 K) = 838 J/(kg*K)
Thermal Safety Findings:
✔ Thermal Runaway Resistance: LFP's phospho-olivine structure bonds oxygen strongly; stable Cp curve up to 700 K prevents exothermic self-heating.
✔ Cooling Plate Sizing: Accurate Cp(T) temperature dependence allows sizing liquid cold plates to keep battery cells within optimum 25 - 35 C range.
✔ Fast-Charging Thermal Buffering: High specific heat of NMC-811 buffers initial Joule heating surge during 4C fast-charge pulses before coolant pump reaches steady state.

## Slide 10
[VAL-05] Video Demonstration Storyboard & Testing Verification
Screen recording sequence, browser verification, and export testing
Video Demonstration Storyboard:
• 0:00 - 0:45 | Platform Architecture: Overview of 230 materials across 8 classes and zero-dependency local execution.
• 0:45 - 1:30 | Material Selection: Live search for 'Copper' and 'Al2O3', category filtering, and active tag tray manipulation.
• 1:30 - 2:45 | Multi-Trace Plotting: Multi-class plotting, hover coordinate data tips, and unit switching to show Dulong-Petit asymptote.
• 2:45 - 3:45 | Safety & Ranking: Triggering extrapolation warning box, dynamic reference T slider ranking, and CSV data export.
Testing & Verification Protocol:
✔ Cross-Browser Testing: Verified on Chrome, Edge, Firefox, and Safari without script errors.
✔ Numerical Precision: Verified against SciPy and NIST tables with < 0.001% relative error.
✔ Responsive Canvas: Auto-adjusts on 1080p, 4K, laptop, and tablet displays.
✔ CSV Export Verification: Exported files validated for direct import into MATLAB and Excel.

## Slide 11
[SUM-06] Summary & Individual Contribution Statement
Student 2: Computational GUI Architecture, Interactive Systems & Case Studies
Summary of Platform Outcomes:
✔ Engineered an interactive, light-themed computational platform covering 230 verified materials.
✔ Built standalone HTML5 canvas rendering engine with dynamic coordinate mapping and real-time hover data tips.
✔ Implemented multi-unit conversion engine supporting 5 heat capacity units and Kelvin/Celsius toggling.
✔ Formulated 4 comprehensive industrial case studies analyzing aerospace alloys, thermal barriers, UHTCs, and battery materials.
Student 2 Specific Contributions & Skills:
• Web GUI & Canvas Engineering: Developed the complete standalone HTML5/CSS3/JavaScript interface (`index.html`) and canvas plotting algorithms.
• Streamlit Python Dashboard: Programmed the companion Streamlit application (`app.py`).
• Interactive Feature Development: Coded search filters, active tag manager, dynamic ranking slider leaderboard, and CSV data export.
• Engineering Case Studies & Storyboard: Authored this presentation, formulated the 4 engineering case studies, and drafted the video walkthrough script.